## Slide 1: STUDY ON PERFORMANCE OF DIFFERENT DYNAMIC TRACK STABLIZER IN USE ON IR By TMM Dte of RDSO

## Slide 2: PERFORMANCE ASPECTS STUDIED
Improvement of lateral ballast resistance at maintenance site just after tamping.
Improvement of lateral ballast resistance at BCM Working site .
Effectiveness of the machine in obtaining the durable section. ( For this the improvement/deterioration in TRC result shall be monitored for three consecutive TRC runs)
Effect of DTS on bridges, tunnels cabins etc.
Settlement and Retention of Cross Level before and after stabilization.
Maintenance and reliability aspect of different machines

## Slide 3: SALIENT FEATURES OF DIFFERENT MACHINES
S. no | Salient Feature | PLASSER DTS | BHEL DTS | METEX DTS
1 | Stabilizing Units | 2 stabilizing units with 4 guide roller | 2 stabilizing units with 4 guide roller | 3 stabilizing units with6 guide roller
2 | Vibration frequency | 0-45 Hz horizontal | 0-45 Hz horizontal | Vertical (0-49 Hz) horizontal (20-25 Hz)
3 | Working Speed | 0-3 kmph | 0-2.5 kmph | 0-2.5 kmph
4 | Vertical preload | 240KN max | 50 - 240KN | 320 KN max
5 | Working Mode | Variable vertical preload (levelling mode)& constant vertical preload (Settlement mode) | Variable vertical preload & constant vertical preload | Variable vertical preload & constant vertical preload
6 | weight | 58 t | 64.5 t | 60t

## Slide 4: M/C PARAMETERS KEPT DURING TRIAL
S. no | Name of machine | Mode of Working | Vibration frequency | Worked Speed | Load Applied
1 | DTS Plasser | settlement | 35 Hz (horizontal) | 1.5kmph | 120
2 | DTS BHEL | settlement | 35 Hz (horizontal) | 1.5kmph | 120
3 | DTS METEX | settlement | 45 Hz (vertical) | 1.5kmph | 160
GENERAL LIFT ON WST WAS KEPT AS 50 mm |  |  |  |  | 

## Slide 5: COMPARATIVE STUDY OF BALLAST RESISTANCE AFTER WORKING OF TAMPING AND DIFFERENT DTS MACHINES
Following measurement were taken:
  Measurement of initial ballast resistance for individual sleeper in consolidated track.
  Measurement of ballast resistance just after tamping
  Measurement of ballast resistance after working of DTS machine
  Method of Measurement of Ballast Resistance
  Rail Post erected just adjacent to the sleeper for taking the reaction.
  Hydraulic Jack with proving ring was used for applying and measuring load in Kg.
  Dial gauge was used on other side to measure deflection.

## Slide 7: BALLAST RESISTANCE AT MAINTENANACE TAMPING SITE
Item | No of Sleepers tested | Average value
Initial ballast resistance | 6 | 1433 Kg
Ballast Resistance just after Tamping | 6 | 663 Kg (46.26% of initial)
Ballast Resistance after working of DTS – Plasser | 6 | 914 kg (63.78% of initial)
Ballast Resistance after working of DTS – METEX | 7 | 836 kg (58.339% of initial)
Ballast Resistance after working of DTS – BHEL | 7 | 767 Kg (53.52% of initial)

## Slide 8: COMPARATIVE STUDY OF BALLAST RESISTANCE AFTER WORKING OF BCM Contd..

## Slide 10: BALLAST RESISTANCE AT BCM SITE
Item | No of sleeper tested | Lateral resistance per sleeper
Ballast Resistance just after Tamping Machine | 4 | 325 kg
Ballast Resistance after , Tamping and DTS M/c - Plasser | 4 | 430 kg (32. 5 % increase)
Ballast Resistance after , Tamping and DTS M/c - METEX | 4 | 415 kg (28 % increase)
Ballast Resistance after , Tamping and DTS M/c - BHEL | 4 | 392.5 kg ( 20.76 % increase)

## Slide 11: EFFECT ON BRIDGES, TUNNELS, BUILDING ETC
NO DIRECT METHOD COULD BE FOUND.
STRESS GENERATED ON RAIL BY THE DIFFERENT MACHINES IS COMPARED WITH THE ONE GENERATED BY TRAIN
INSTRUMENTED RAIL WAS USED FOR THE PURPOSE

## Slide 12: EFFECT ON BRIDGES, TUNNELS, BUILDING ETC Contd…
A 6.76 METER RAIL WAS PREPARED .
STRAIN GAUGES ON THREE LOCATIONS AT EQUAL DISTANCE TO ACCOMMODATE THEM IN BETWEEN THE SLEEPER CENTRE.
3 NOS. OF STRAIN GAUGES (10MM SIZE-120 OHMS) WERE FIXED AT THREE

## Slide 13: FIXING OF STRAIN GAUGES

## Slide 15: STRESS GENERATED BY DTS
Case | Maxm Tensile stress Kg/sqcm | Maxm Compressive stress Kg/Sqcm
Passenger Train | 484 | 272.25
Goods Train | 665.5 | 423.5
M/S Plasser and Theurer DTS | 514.25 | 332.75
M/S BHEL- DTS | 605 | 302.5
M/S METEX- DTS | 786.5 | 847

## Slide 16: MEASUREMENT OF CROSS LEVEL AND SETTLEMENT BEFORE AND AFTER STABILIZING.
Machine | Settlement after DTS | Max modification of X-L by DTS
Plasser | 4-8 mm | 3 mm
Metex | 3-14 mm | 4 mm
Bhel | 2-6 mm | 2 mm

## Slide 17: FURTHER STUDY TO BE DONE
RATE OF INCREASE OF CONSOLIDATION UNDER TRAIN LOAD (ONE DTS RUN EQUIVALENT TO HOW MUCH GMT) .
RETENTIVITY OF TRACK PARAMETERS AFTER PASSING OF TRAIN WHEN DTS IS NOT USED AND WHEN DTS IS USED.
RELATION BETWEEN GENERAL LIFT AND LOSS OF CONSOLIDATION.

## Slide 18: CONCLUSION
IMMEDIATELY AFTER TAMPING , BALLAST RESISTANCE IS REDUCED TO 46 % OF ORIGINAL VALUE. IMMEDIATE CONSOLIDATION BY DTS INCREASES IT BY 38 %.
THUS:
  RETENTION OF TRACK PARAMETERS AFTER PASSING OF TRAIN SHOULD BE BETTER.
  DURING SUMMER IT IS ALL THE MORE IMPORTANT TO USE DTS TO RECOUP LATERAL BALLAST RESISTANCE IMMEDIATELY AFTER TAMPING.

## Slide 19: CONCLUSION Contd…
PLASSER AND BHEL DTS DOES NOT GENERATE STRESS MORE THAN THAT BY TRAIN AND ARE SAFE FOR BRIDGES AND BUILDINGS FROM STRESS CONSIDERATION.
HOWEVER RESONANCE EFFECT TO BE TAKEN SEPARATELY.

## Slide 20
THANK YOU

## Slide 21
BHEL Driving and vibration is electrically operated. Traction motor is used for driving.